## Slide 1: HFM Test Station Main Cryostat
Arnaud Vande Craen (TE-MSC)
TE-MSC-CMI – Section Meeting 19/02/2013

## Slide 2: Summary
Introduction
Concept
Design

## Slide 3: Introduction

## Slide 4: What ?
High Field Magnet Test Station
Vertical Cryostat
Temperature : 1.9 K
Maximum pressure : 5 bar
As much polyvalent as possible

## Slide 5: Why ?

## Slide 6: Why ? (2)
FRESCA 2 Magnet
  Up to
    2.5 m long
    1.5 m diameter
    8 tons
  Nb3Sn strands
  Maximum current : 20 kA
  Maximum field : 13 T
    (LHC ≈ 8.3T)

## Slide 7: Why ? (3)
Large cryostat for magnet test
  Polyvalent
    FRESCA 2 (CERN)
    HTS dipole insert (CERN)
    LD1 (Berkeley)
  Temperature control (cool down)
    Magnet sensitive to strain
  Maximum current test
  Field analysis (future)
  Quench
    Protection
    Detection
    Analysis

## Slide 8: How ?
Main cryostat
  Magnet cool down
  Magnet powering
Valve box
  Cryogenic control
Cold buffer
  Store helium in case of quench
2 power supply
  Main magnet (20 kA)
  Insert magnet (10 kA)

## Slide 9: How ? (2)
Cold buffer
Main cryostat
Valve box

## Slide 10: Where ? (1)
Horizontal test benches
Vertical test benches

## Slide 11: Where ? (2)
HFM cryostat
20 kA power Converter
Dump Resistor
Control Room
Valve box
Cold buffer
Cryogenic Control
Cryogenic rack
10 kA power Converter
Installed
Pumping line

## Slide 12: Concept

## Slide 13: Philosophy
Vertical test station
  Easy magnet insertion
  Easy electrical connection
    Current leads
    Instrumentation
  Limit cryogenic connections during magnet insertion
  No dedicated helium vessel for magnet

## Slide 14: Principle
Claudet bath
  Helium @ 1 bar
    4.2 K – 300 K
    1.9 K (controlled)
  Helium @ 16 mbar
    1.8 K

## Slide 15: Concept (1)
Neck
Lambda plate
Lower volume
Heat exchanger
1
2
3
4

## Slide 16: Concept (2)
Vacuum vessel
  Supported by brackets
Helium vessel
  Hanging to top cover
Magnet
  Hanging to lambda plate
Lambda plate
  Hanging to top plate
Top plate
  Fixed to top cover

## Slide 17: Design

## Slide 18: Vacuum vessel
Dimensions
  4.6 m height
  2.3 m diameter
  4.8 tons
Stainless steel (304L)
Conical cover
3 supports
Static vacuum

## Slide 19: Vacuum vessel (2)
Conical cover
  Support magnet weight
  Limit deformation
Vacuum vessel protection
  Burst disk (DN200)
  Exhaust line (DN300)
Jumper
  Connection to valve box
  Regroup all cryogenic lines

## Slide 20: Helium vessel
Neck
  3 mm thick
  1.6 m diameter
  1.6 m long
  Thermalisation (limit heat in leak)
Lower volume
  6 mm thick
  1.5 m diameter
  2.5 m long
Max pressure : 5 bar
1.9K
4.2K
300K

## Slide 21: Helium vessel (2)
Jumper
  Regroup all lines
Fixed point
  Avoid lines movement
Thermalisation
  Welded ?
  Brazed ?

## Slide 22: Helium vessel (3)
Heat exchanger
  Copper tube brazed to stainless steel tube
  U shape welded to flange (30 x)
  Closed box to pump
  Cooling power ≈ 100 W @ 1.9K
    (1.5 day Cool-Down)

## Slide 23: Thermal shield
Actively cooled
Supported from top cover
Stainless steel structure
Copper
  Sheet
  Pipe brazed

## Slide 24: Insert
Top plate
  Current leads (20 kA & 10 kA)
  Instrumentation
Radiative screens
  Limit heat in leak
Lambda plate (50 mm thick)
  Stainless steel
  Lambda valve
  Splices
  Instrumentation
Mechanical support
  Lambda plate to top plate
  Magnet (15 tons) to lambda plate