## Slide 1: TE-MSC-CI Section
Activities present and future

## Slide 2: Summary of main activities
LHC Operation
  Cryo-magnet coordination
  The new storage building
  Components procurement
  Section support to LHC: MP3 and patroller
  X-ray tomography and its mock-up
  Participation to LHC Splices Task Force
  Interventions for future shutdown
LHC Upgrade
  DS Collimators (HL-LHC)
  New inner triplet
Other projects and activities
  HIE-ISOLDE
  SPL
  ITER (Plugs, Support posts)
  CERN/France collaboration

## Slide 3: LHC Operation

## Slide 4: Cryomagnet coordination
Dipoles
23 cold tested and ok
  7 without vacuum vessel
9 ready for cold test
1 being cryostated
11 being repaired
In total 44 dipoles available
Quadrupoles
3 cold tested and ok
4 to be tested
8 to be repaired
Special magnets
Q8-Q10
  1 available
Q7
  1 available
Q7-Q10
  1 to be repaired (QH’s)
Inner triplets (Q1-Q3)
  One each available (3)
  To be tested (tested in US)
D1-D4
  One each available (4)
  To be tested (tested in US)
December 2010

## Slide 5: Building 189
New storage building
SMI2
189
375 m2
Budget <400 kCHF
For storage of
cryostats and
interconnections
components

## Slide 6: Components procurement
Cold Support Posts
  LHC spare
  Short connection cryostats
  DS collimators
  ITER and INFN
W bellows
  Firms selected
  Tender document under preparation
Vacuum vessels
  Some units procured by French Collaboration (CNRS)
  Call for tender to launch for the other ones

## Slide 7: Section support to LHC operation
MP3 shifts and stand-by
Help for patrols

## Slide 8: X-Ray tomograph
Mock-up manufacturing and maintenance
Simulation to assess safety of transport with LHe in cold masses
   Authorization given
Optimization of image quality

## Slide 9: Splice task force
Inventory and synthesis schemes of the 94 6kA circuits
Setup for a performance and validation test
  Voltage taps on in and out cables
  3 connections in series
  Design validated

## Slide 10: Splice task force
Participation to the cold testing of 13kA shunts
Preparation of the SSSs for test
  Instrumentation
  Quench stopper
  Helium tank

## Slide 11: Interventions during long shutdown
# | Description | Quantity | Location | Remark
1 | DS Collimators at P3 | 34 cryo-assemblies | IR3 (L&R) | End of shutdown
2 | Cryomagnets replacement | ≈ 10 ? | Everywhere | For NC or high int. splice resistance
3 | Splices investigation | ≈ 10 ? | Everywhere | 13kA, 6kA (see tomorrow), 600A (N)
4 | Circuits issues | 3 so far | Located | Open, high R
5 | DFBA splices | 16 units | Arc extremities | To be decided
6 | Consolidation of CC | 2 | L8,L1 (L3) | But all to be inspected
7 | Plug-in Modules | ? | Everywhere | Endoscopy ? Cleaning ?
8 | Y_lines | 3 | 3 arcs | 
9 | DN200 | ≈ 600 | 3 arcs | 
10 | SAM | 2 | R2, L8 | DN160 & He gauges
11 | RP samples | ? | Arc 45 | To install in other arcs?
12 | Interventions on new NCs | 15 % | Everywhere | Quick reaction
13 | Vacuum leaks | 11-20 | Everywhere | 
14 | Q5L8 replacement | 1 | MSL8 | 
15 | Triplet braid | 2 | P2 & 8 | To be confirmed
Management of the “special activities”
Interconnections thermal shield modification
  No more grinding of machine welds
  Better reliability

## Slide 12: LHC Upgrade

## Slide 13: DS Collimators
Supervises the design changes
Follows-up the integration study for IR3 (both cold and warm)
Coordinates the execution of the Work Packages
Coordinates the installation of the equipment

## Slide 14: DS Collimators Integration
Design of shortened connexion cryostats
  4,5 m shorter
  2 support posts
  Remove lead shielding
  Displacement of shuffling module
  Include all ECR
    Sliding supports
    Lira insulation
    Stainless Steel shield

## Slide 15: New inner triplets
Cryostat for short test magnet

## Slide 16: Other projects

## Slide 17: HIE Isolde
Design of vacuum vessel
  Shape and thickness
  Opening
  Selection of seals
Integration of components
  Cavities
  Solenoid
  Warm steerer
  Thermal shield
  Cryogenic components

## Slide 18: HIE Isolde
Assembly procedure
  Opening of vacuum vessel
  Insertion in vacuum vessel
Functional specification written for high energy cryomodule
Vacuum vessel for testing of B-Cam alignment instrumentation

## Slide 19: SPL
Responsible of WG3 : Cryomodule design
  Part of the “SPL Study”
  Collaboration with CNRS/CEA
Design of a 4 cavities cryo-module
  Learning of the critical assembly phases
  Proof of concept of innovative coupler based supporting system
  Explore cryogenic operation issues

## Slide 20: SPL
Integration of components
  Equipped cavities
  Couplers
  Thermal and magnetic shield
  Cryogenic components
Design of tooling for cryostating
Engineering specification (for end of 2010)

## Slide 21: ITER
Design, manufacture and test a prototype plug
  Tightness requirement less strict than LHC ones
  All the electrical insulation layers have to be kept
First prototype well within specification
  But only one cable
  The extremities tightness will be important
Next prototype (in collaboration with MSC-ML)
  Based on the acquired technology
  15 crossing cables
  Objective : same results in terms of pressure resistance,
  leak tightness and electrical insulation
  To be available beginning of 2011

## Slide 22: ITER
Cold supports post testing
  Study and build of a dedicated tests set-up
  Modify the existing test bench
  Execute the tests on 5 columns
Give view on mechanical properties
Follows-up of conclusions

## Slide 23: Protocole de Collaboration K1597/DG
Collaboration CERN-CEA-CNRS/IN2P3
Signed in December 2008
Value of contribution : 11.258.900 Euros
  7.056.000 Euros in components
  4.202.900 Euros in manpower
5 technical accord ongoing
  Linac 4
  SPL
  New superconducting magnets
  CLIC
  Study on accelerators and components supply

## Slide 24: Future

## Slide 25: Work plan for 2011
LHC Operation
  Cryo-magnet coordination
  Spares cryostating
  Support during operation : MP3 and Patrols
  Procurement and storage of components
  X-Ray tomography expertise

## Slide 26: Work plan for 2011
LHC Consolidation, Upgrade and Maintenance
  DS Collimators
    Shortened connection cryostats
    Technical coordination
    Installation
  Follow-up and support to LHC splices task force
    6 kA splices
    Shunt test in SM18
    General
  Preparation of next long shutdown special activities
  Optimization of Interconnection thermal shield
  Cryostating of MQXC

## Slide 27: Work plan for 2011
Other projects
  HIE-Isolde : Cryomodule design
  SPL
  ITER: Plugs and general consultancy
  FRESCA 2 cryostat
  CERN/France collaboration agreement management